## Slide 1: ES2 – AC3E Battery testing plan

## Slide 2: Cell Choice
We are interested in testing wither 21700 or 18650 cells in both system and cell level

## Slide 3: Model Geometry
20 cylindrical cells, type 21700
  21 mm diameter
  70 mm height
  5s4p configuration (5 serial strings of 4 parallel cells)
Offset packaging
Plastic holder frames
Serial and parallel connectors
Thin plastic wrapping around the entire pack
Cell malfunction after 1 min
Connectors
Plastic Wrapping
Cell Holder
Terminals

## Slide 4: Cell details
The commercial NCM811-21700 cylindrical lithium-ion battery cell had a cathode containing approximately 80% nickel, 10% cobalt, and 10% manganese, with a diameter of 21 mm and a length of 70 mm

## Slide 5: Model Definition
The figure shows the model geometry
Three 21,700 battery cylinders (21 mm in diameter, 70 mm high) are placed adjacent to each other
Small connecting strips of aluminum are located at the top and bottom of the cylinders according to the 6s2p configuration
The whole pack is assumed to be wrapped in plastic, forming a domain filled with air
Geometry 1

## Slide 6: Model Definition
Assuming a nominal capacity of 4 Ah for each cell and nominal voltage of 3.7 V, the battery pack has a total nominal capacity of approximately 178 Wh
Geometry 1

## Slide 7: Model Setup
Battery Pack
  Shared cell settings, defining one individual battery model in each cylinder
  Current conduction in the connectors
  Battery pack is charged at end terminals
    2C current
    Starting at 25% SOC with cutoff at 21 V
  Thermal Event nodes
    Explicit at 1 min for one cell
    When temperature exceeds 80 °C for remaining cells
    Ohmic resistances of batteries increased when events are triggered

## Slide 8: Model Setup
Heat Transfer
  Anisotropic thermal conductivities in all cylinders define the jelly roll winding
  Cooling by convection
Electrochemical Heating Multiphysics node
  2-way coupling of heat sources and temperature
  Heating due to
    Joule heating in conductors
    Electrochemistry inside cells
    Thermal events